## Slide 1
THE MICROLAB
Mini Greenhouse Monitor
Mini Greenhouse Monitor
A MicroLab Curriculum Module
ESP32 · MicroPython · DHT11 · Capacitive Moisture · Dual OLED · Google Sheets
6
Modules
3
Sensors
2
OLEDs
1
Dashboard

## Slide 2
Project Overview
Introduction
The Real-World Problem
Millions of people — the elderly, those with disabilities, and low-income families — struggle to grow their own food reliably. Traditional gardening requires constant monitoring that isn't always possible. Smart agriculture technology is changing this, and the students who build it are in high demand.
What We Build
A plexiglass greenhouse enclosure with live temperature, humidity, and soil moisture monitoring displayed on two OLED screens.
Data Collection
Sensor readings sent to Google Sheets every 5 minutes. Students analyze trends and learn data-driven decision making.
AI Integration
Tier 1: AI-assisted coding. Tier 2: Threshold-based automated decisions. Tier 3: Edge ML soil classification.
Career Connection
AgTech, biomedical monitoring, precision agriculture, GE Aerospace environmental systems — all use this exact technology.

## Slide 3
Hardware List
Bill of Materials
Components Required
1
ESP32 30-pin Dev Board
Main microcontroller — runs MicroPython, broadcasts WiFi AP
Seeed Studio / Amazon
2
DHT11 Sensor
Temperature & Humidity — 3-pin module
Amazon
3
Capacitive Moisture Sensor
Soil moisture — TLC555I chip version (DIYables 4-pack)
Amazon
4
SSD1306 OLED Display x2
128x64 I2C — 0.96" displays for live data
Amazon / Seeed Studio
5
Jumper Wires
Male-to-male and male-to-female assorted
Amazon
6
Breadboard
Full-size 830-point for prototyping
Amazon
7
Micro USB Cable
For programming via Thonny IDE
Amazon
8
Plexiglass Enclosure
Pre-built greenhouse shell for final assembly
MicroLab provided

## Slide 4
Wiring Reference
Hardware Setup
Pin Connections — ESP32 → Sensors
Component / Pin
GPIO
Notes
DHT11 — Data
GPIO 4
10kΩ pull-up to 3.3V recommended
DHT11 — VCC
3.3V
DHT11 — GND
GND
Moisture — AOUT
GPIO 32
Confirmed best ADC pin on this board
Moisture — VCC
5V (VIN)
Sensor requires 5V for proper output
Moisture — GND
GND
OLED #1 SDA (Temp/Hum)
GPIO 21
I2C Bus 1
OLED #1 SCL (Temp/Hum)
GPIO 22
I2C Bus 1
OLED #2 SDA (Moisture)
GPIO 26
I2C Bus 2 (SoftI2C)
OLED #2 SCL (Moisture)
GPIO 27
I2C Bus 2 (SoftI2C)
⚠ OLED #1 and OLED #2 must be on separate I2C buses — both have address 0x3C

## Slide 5
MODULE 1
OLED Display #1
Temp / Humidity Display — I2C Bus 1 (SDA=21, SCL=22)
1 / 6

## Slide 6
Module 1 — OLED #1 Test
Black Box Step 1 of 4
Objective: Confirm OLED #1 is detected and displays text before adding sensors.
Step 1 — I2C Scan
from machine import SoftI2C, Pin i2c1 = SoftI2C(scl=Pin(22), sda=Pin(21)) print("Bus 1:", [hex(d) for d in i2c1.scan()])
✓ Expected: Bus 1: ['0x3c']
Step 2 — Display Test
from machine import SoftI2C, Pin import ssd1306 i2c1 = SoftI2C(scl=Pin(22), sda=Pin(21)) oled = ssd1306.SSD1306_I2C(128, 64, i2c1) oled.fill(0) oled.text("MicroLab", 24, 10) oled.text("OLED #1 OK!", 16, 44) oled.show()
Troubleshooting
⚡ Nothing found on Bus 1
→ Check SDA→GPIO21 and SCL→GPIO22 wiring
⚡ AttributeError: SSD1306_I2C
→ Wrong ssd1306.py — replace with official MicroPython version
⚡ Display stays blank
→ Check VCC→3.3V and GND connections

## Slide 7
MODULE 2
OLED Display #2
Moisture Display — I2C Bus 2 (SDA=26, SCL=27)
2 / 6

## Slide 8
Module 2 — OLED #2 Test
Black Box Step 2 of 4
Objective: Confirm OLED #2 is on a separate I2C bus and both displays work simultaneously.
Why Two Buses?
Both OLEDs share the same I2C address (0x3C). If connected to the same bus they will conflict and only one will respond. The solution is to use two separate I2C buses on the ESP32.
Both OLEDs Test
from machine import SoftI2C, Pin import ssd1306 i2c1 = SoftI2C(scl=Pin(22), sda=Pin(21)) i2c2 = SoftI2C(scl=Pin(27), sda=Pin(26)) oled1 = ssd1306.SSD1306_I2C(128, 64, i2c1) oled2 = ssd1306.SSD1306_I2C(128, 64, i2c2) oled1.fill(0)
oled1.text(
"OLED #1 OK!", 16, 30) oled1.show() oled2.fill(0)
oled2.text(
"OLED #2 OK!", 16, 30)
oled2.show()
Common Mistake
Both OLEDs on same pins (21/22): → i2c.scan() only finds ONE device → Second OLED never responds → Code crashes on second oled.show() Fix: Move OLED #2 to GPIO 26 (SDA) and GPIO 27 (SCL)
✓ Expected: Both screens light up simultaneously with different text

## Slide 9
MODULE 3
DHT11 Sensor
Temperature & Humidity — GPIO 4
3 / 6

## Slide 10
Module 3 — DHT11 Sensor Test
Black Box Step 3 of 4
Objective: Confirm DHT11 reads temperature and humidity before integrating with OLEDs.
Wiring
VCC
3.3V
GND
GND
DATA
GPIO 4
Note: Add 10kΩ pull-up resistor
between DATA and 3.3V if errors occur
Test Code
import dht import time from machine import Pin sensor = dht.DHT11(Pin(4)) while True: sensor.measure() temp = sensor.temperature() hum = sensor.humidity() print("Temp: {}C Hum: {}%" .format(temp, hum)) time.sleep(2)
✓ Expected: Temp: 25C Hum: 45% (values will vary with room conditions)
Troubleshooting
⚡ ETIMEDOUT error
→ Wrong pin — try the pin scan test. Add 10kΩ pull-up resistor
⚡ Bad sensor
→ Replace DHT11 — they fail silently. Always test with known-good sensor

## Slide 11
MODULE 4
Capacitive Moisture Sensor
Soil Moisture — GPIO 32 (ADC)
4 / 6

## Slide 12
Module 4 — Moisture Sensor Test
Black Box Step 4 of 4
Objective: Confirm the capacitive moisture sensor reads correctly and calibrate dry/wet values.
USE DIYS TLC555I sensor -- TLC555I sensor — cheap v1.2 clones have known quality issues
Pin Order (left to right):
AOUT
GPIO 32
Analog signal output
GND
GND
VCC
5V (VIN)
Must be 5V — 3.3V gives weak output
Calibration Test
from machine import Pin, ADC import time adc = ADC(Pin(32)) adc.atten(ADC.ATTN_11DB) print("IN AIR:") for i in range(5): print("Raw:", adc.read()) time.sleep(1) # Then dip in water and repeat # Air value = DRY_VAL (~3000-4095) # Water value = WET_VAL (~1000-1800)
✓ Confirm values change clearly between air and water
Record your values:
DRY_VAL =
______ (sensor in open air)
WET_VAL =
______ (sensor in water)

## Slide 13
MODULE 5
Full Integration
All Components Together — Live Greenhouse Monitor
5 / 6

## Slide 14
Module 5 — main.py (Full Code)
Integration
Objective: Combine all tested components into one running program.
Files Required on ESP32
main.py
Main program — provided in this module
ssd1306.py
Official MicroPython OLED driver — must be official version
Key Configuration Values to Update
# ── Update these three values from your calibration session ── DRY_VAL = 4095 # Your air reading from Module 4 WET_VAL = 1321 # Your water reading from Module 4 ENABLE_WIFI = False # Set True to enable Google Sheets logging
What You Should See
1
Splash screen on both OLEDs showing 'MicroLab Greenhouse v2' + WiFi status
2
OLED #1: Live temperature (°C) and humidity (%) updating every 10 seconds
3
OLED #2: Live moisture percentage and DRY / OK / WET status label

## Slide 15
MODULE 6
Google Sheets Dashboard
Data Collection & Analysis — Tier 1 AI Integration
6 / 6

## Slide 16
Module 6 — Google Sheets Setup
Data Collection
Objective: Enable WiFi logging so sensor data builds a live dataset in Google Sheets.
Setup Steps
1
Create a new Google Sheet — name it 'Greenhouse Monitor'
2
Click Extensions → Apps Script → paste apps_script.js
3
Click Deploy → New Deployment → Web App → Anyone → Deploy
4
Copy the Web App URL
5
In main.py: set ENABLE_WIFI=True, add SSID, password, and URL
6
Upload main.py and reboot — data appears in Sheets every 5 min
What the Sheet Captures
Timestamp
Auto-formatted date & time
Temperature (°C)
DHT11 reading
Humidity (%)
DHT11 reading
Moisture (%)
Calibrated 0-100%
Moisture Raw
Raw ADC value
Status
DRY / OK / WET label
AI Integration Path: Tier 1 — use AI to analyze sheet data and write threshold alerts | Tier 2 — Edge Impulse soil classification model deployed to ESP32

## Slide 17
Student Challenge Card
Extend Your Greenhouse
You built it — now make it smarter.
1 Beginner
Add a buzzer that beeps when moisture drops below DRY threshold
2 Intermediate
Add a relay and small pump — auto-water when soil is DRY
3 Advanced
Use Edge Impulse to train a model that predicts when watering is needed based on historical data
4 Expert
Build a multi-plant system with 3 sensors and a dashboard showing all zones in Google Sheets

## Slide 18
Career Connections
Workforce Pathway
Skills You Built in This Module
I2C Communication
Industry standard protocol used in every embedded system
Sensor Calibration
Critical skill in biomedical, AgTech, and manufacturing QA
Data Logging
Every modern manufacturing system logs sensor data continuously
MicroPython / Embedded C
Language of IoT devices — 67,000+ unfilled Ohio tech roles
Cloud Integration
Google Sheets → SQLite → dashboards — the full data pipeline
Cincinnati Employers Using These Skills: GE Aerospace · P&G · Bosch · Kroger Distribution · Cincinnati Children's Hospital